## Slide 1: WELCOME Clock School 101
What you’ll learn from your synchron® motor
  Distinguishing Information
    Model # explanation
    Voltage, speed, cycles
    Mounting characteristics
    Wire colors
  Replacement options
    Mechanical
    Solid-state

## Slide 2: Scott DeSmith
Product Application Specialist
Scott has been with American Time for the past 33 years. As a Product Application Specialist, customers continuously rely on Scott’s expertise in traditional synchronized time system solutions and legacy clock repairs to troubleshoot and solve their clock pain points.
Your presenter today
Notes: Talk about questions answered at end. As questions com up, use chat feature during presentation.

## Slide 3: About Synchron® Motors
The ones we will be looking at today are most commonly use in:
  HVAC – Damper and Valve Controls
  Mechanical Timers
  Clocks!
  Chart Recorders
  POP Displays
Made by Hansen Corporation in many types for a wide variety of applications.
  The founder was a jeweler and watch maker and gained recognition when he designed the first automatic bell ringing system at the request of a local high school principal.
Notes: Point out interesting fact about the founder of the Hansen Corporation.

## Slide 4: How to read your Synchron Motors
Model #
Sample: A 12 R A -3
V, Hz, RPM
Other Information
Date Stamp, Custom Models
Voltage, Speed
Notes: Mention sample model # going to be used in next several slides

## Slide 5: Sample Model # A 12 R A -3
Alphabetical characters shown in this position signify motor types.
  Include lead length and stripping, lead position, lead color code and torque rating of motor.
  EXAMPLE: “A” means 6” leads stripped 5/8 and in 6 o’clock position (standard), color (black 110v. 60cy.) and standard torque (3w) 8 in. oz. @ 1RPM.

## Slide 6: Sample Model # A 12 R A -3
Numeral after motor type is the type of output.
  Diameter and length of hub, diameter and length of shaft and whether round, flatted, threaded or with pinion, crank or other device.

## Slide 7: Sample Model # A 12 R A -3
Letter R (or L) signifies direction of rotation of shaft.
  R=Clockwise and L=Counterclockwise when viewing output side of motor.

## Slide 8: Sample Model # A 12 R A -3
Letter shown after “R” or “L” represents the style of mounting.
  “A” in this instance is a round motor with 4 mounting lugs.

## Slide 9: Sample Model # A 12 R A -3
Called dash numbers and is a hyphenated numeral denoting a special motor feature series.
  Internal clutches, special tests, thrust positions Up or Down, reversible and tandem, plated motors & etc.

## Slide 10: Voltage, Speed and Other Information
Output shaft speeds listed in RPM, RPH or RPD
Input volts
Cycles / Hz
Date stamping

## Slide 11: Replacement Options
Mechanical
Repair/Replace
Solid-State Movement
Replace
Energy Savings
Circuit Board & Cover
Molex® Connection

## Slide 12: This ends our webinar
A recording of this has been made and will be available to you. Watch for email.
Thank You For Joining Us Today
  Watch for upcoming Clock School webinars
    Let us know what topics you’d like us to cover!
    email us: marketing@atsclock.com
  Subscribe to our Blog for current topics
    blog.american-time.com
  Contact us
    800-328-8996
    american-time.com
Notes: At this time answer any questions that may have come up as time permits.
Talk about watching for upcoming webinars. Future topic recommendations.